## Slide 1: Lecture 09 – Image segmentation II Thresholding
Prof. João Fernando Mari
joaofmari.github.io
joaof.mari@ufv.br
SIN 392 – Introduction to Digital Image Processing (2023)

## Slide 2: Agenda
Thresholding
Basic global thresholding
Otsu’s method

## Slide 3: Thresholding
Image thresholding:
  Central position in image segmentation applications
  Ease of implementation
  Computational speed
Global thresholding:
  T is a constant applicable to an entire image
Local threshold (variable or regional):
  T changes throughout the image
T

## Slide 4: Thresholding
Image thresholding:
  Central position in image segmentation applications
  Ease of implementation
  Computational speed
Global thresholding:
  T is a constant applicable to an entire image
Local threshold (variable or regional):
  T changes throughout the image
T

## Slide 5: Basic global thresholding

## Slide 6: Basic global thresholding
Select an initial guess for the global threshold, T.
Segment the image using T:
  Isso dará origem a dois grupos de pixels:
    G1, pixels com valores de intensidade > T;
    G2, pixels com valores ≤ T.
Calcular os valores de intensidade média m1 e m2 para os pixels em G1 e G2 , respectivamente.
Calcular um novo valor de limiar:
Repetir as etapas 2 a 4 até que a diferença entre os valores de T em iterações sucessivas seja menor que o parâmetro predefinido ∆T.

## Slide 7: Basic global thresholding
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
Image I
T0 = min(I) = 0
∆T = 0.001
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 8: Basic global thresholding
T0 = min(I) = 0
G1 = [2, 3, 6, 5, 3, 1, 1, 1, 6, 7, 6, 3, 5, 7, 3]
G2 = [0]
m1 = (2 + 3 + 6 + 5 + 3 + 1 + 1 + 1 + 6 + 7 + 6 + 3 + 5 + 7 + 3) / 15 = 59 / 15 = 3.9333
m2 = 0 / 1 = 0
T1 = (3.9333 + 0) / 2 = 1.9667
|T1 – T0| = |1.9667 – 0| = 1.9667 > ∆T. Then, new iteration.
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
Image I
T0 = min(I) = 0
∆T = 0.001
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
T0
T1
∆1

## Slide 9: Basic global thresholding
T1 = 1.9667
G1 = [2, 3, 6, 5, 3, 6, 7, 6, 3, 5, 7, 3]
G2 = [1, 1, 1, 0]
m1 = (2 + 3 + 6 + 5 + 3 + 6 + 7 + 6 + 3 + 5 + 7 + 3) / 12 = 56 / 12 = 4.6667
m2 = (1 + 1 + 1 + 0) / 4 = 3 / 4 = 0.75
T2 = (4.6667 + 0.75) / 2 = 2.7084
|T2 – T1| = |2.7084 – 1.9667| = 0.7417 > ∆T. Then, new iteration.
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
Image I
T0 = min(I) = 0
∆T = 0.001
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
T0
T1
∆1
T2
∆2

## Slide 10: Basic global thresholding
T2 = 2,7084
G1 = [3, 6, 5, 3, 6, 7, 6, 3, 5, 7, 3]
G2 = [2, 1, 1, 1, 0]
m1 = (3 + 6 + 5 + 3 + 6 + 7 + 6 + 3 + 5 + 7 + 3) / 11 = 54 / 11 = 4.9091
m2 = (2 + 1 + 1 + 1 + 0) / 5 = 1
T3 = (4.9091 + 1) / 2 = 2.9546
|T3 – T2| = |2.9546 – 2,7084| = 0.2462 > ∆T. Then, new iteration.
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
Imagem I
T0 = min(I) = 0
∆T = 0.001
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
T0
T1
∆1
T2
∆2
T3
∆3

## Slide 11: Basic global thresholding
T3 = 2.9546
G1 = [3, 6, 5, 3, 6, 7, 6, 3, 5, 7, 3]
G2 = [2, 1, 1, 1, 0]
m1 = (3 + 6 + 5 + 3 + 6 + 7 + 6 + 3 + 5 + 7 + 3) / 11 = 54 / 11 = 4.9091
m2 = (2 + 1 + 1 + 1 + 0) / 5 = 1
T4 = (4.9091 + 1) / 2 = 2.9546
|T4 – T3| = |2.9546 – 2.9546| = 0.0 <= ∆T. Then, end of the algorithm.
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
Image I
T0 = min(I) = 0
∆T = 0.001
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
T0
T1
∆1
T2
∆2
T3,4
∆3

## Slide 12: Basic global thresholding
T3 = 2.9546
G1 = [3, 6, 5, 3, 6, 7, 6, 3, 5, 7, 3]
G2 = [2, 1, 1, 1, 0]
m1 = (3 + 6 + 5 + 3 + 6 + 7 + 6 + 3 + 5 + 7 + 3) / 11 = 54 / 11 = 4.9091
m2 = (2 + 1 + 1 + 1 + 0) / 5 = 1
T4 = (4.9091 + 1) / 2 = 2.9546
|T4 – T3| = |2.9546 – 2.9546| = 0.0 <= ∆T. Then, end of the algorithm.
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
Image I
Image I’
T0 = min(I) = 0
∆T = 0.001
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
T4

## Slide 13: Otsu’s method

## Slide 14: Otsu’s method
Calculate the normalized histogram of the input image:
  Designar os componentes do histograma como pi, i = 0, 1, ..., L-1.
Calculate the accumulated sums, P1(k), for k=0, 1, 2, ..., L-1, according to:
Calculate the accumulated means m(k), for k=0, 1, 2, ..., L-1, according to :
Calculate the global mean intensity, mG, according to :
Calcular a variância entre classes, , para k=0, 1, 2, ..., L-1, de acordo com:
  , reescrita como:
O limiar de Otsu, k*, é valor de k para o qual é máxima.
  Se ocorrer mais de uma máxima, K* é a média dos valores de k correspondentes
Obter a medida de separabilidade, η*, considerando k = k* na equação:
  , em que:

## Slide 15: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 |  |  |  |  | 
1 | 3 | 0.1875 |  |  |  |  | 
2 | 1 | 0.0625 |  |  |  |  | 
3 | 4 | 0.2500 |  |  |  |  | 
4 | 0 | 0.0000 |  |  |  |  | 
5 | 2 | 0.1250 |  |  |  |  | 
6 | 3 | 0.1875 |  |  |  |  | 
7 | 2 | 0.1250 |  |  |  |  | 
 | 16 | 1.0 |  |  |  |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 |  |  |  |  | 
1 | 3 | 0.1875 |  |  |  |  | 
2 | 1 | 0.0625 |  |  |  |  | 
3 | 4 | 0.2500 |  |  |  |  | 
4 | 0 | 0.0000 |  |  |  |  | 
5 | 2 | 0.1250 |  |  |  |  | 
6 | 3 | 0.1875 |  |  |  |  | 
7 | 2 | 0.1250 |  |  |  |  | 
 | 16 | 1.0 |  |  |  |  | 
Image I
16 pixels (4 x 4)
3 bits = 8 gray levels.
[0, ..., 7]
2 | 3 | 6 | 5 | 
3 | 1 | 1 | 1 | 
6 | 7 | 6 | 3 | 
5 | 7 | 0 | 3 | 
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 16: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 |  |  |  | 
1 | 3 | 0.1875 | 0.2500 |  |  |  | 
2 | 1 | 0.0625 | 0.3125 |  |  |  | 
3 | 4 | 0.2500 | 0.5625 |  |  |  | 
4 | 0 | 0.0000 | 0.5625 |  |  |  | 
5 | 2 | 0.1250 | 0.6875 |  |  |  | 
6 | 3 | 0.1875 | 0.8750 |  |  |  | 
7 | 2 | 0.1250 | 1.0000 |  |  |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 |  |  |  | 
1 | 3 | 0.1875 | 0.2500 |  |  |  | 
2 | 1 | 0.0625 | 0.3125 |  |  |  | 
3 | 4 | 0.2500 | 0.5625 |  |  |  | 
4 | 0 | 0.0000 | 0.5625 |  |  |  | 
5 | 2 | 0.1250 | 0.6875 |  |  |  | 
6 | 3 | 0.1875 | 0.8750 |  |  |  | 
7 | 2 | 0.1250 | 1.0000 |  |  |  | 

## Slide 17: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 |  |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 |  |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 |  |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 |  |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 |  |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 |  |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 |  |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 |  |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 |  |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 |  |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 |  |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 |  |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 |  |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 |  |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 |  |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 |  |  | 

## Slide 18: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 |  |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 |  |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 |  |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 |  |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 |  |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 |  |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 |  |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 |  |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 |  |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 |  |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 |  |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 |  |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 |  |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 |  |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 |  |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 |  |  | 
3.6875

## Slide 19: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 
3.6875

## Slide 20: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 
3.6875

## Slide 21: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 
3.6875

## Slide 22: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 0.84985
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 1.35425
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 0.17798
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 0.11816
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 0.00000
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 0.21533
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 1.00269
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 1.37158
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 0.84985
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 1.35425
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 0.17798
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 0.11816
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 0.00000
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 0.21533
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 1.00269
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 1.37158
5.08984
3.6875
em que:

## Slide 23: Otsu’s method
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 0.84985
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 1.35425
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 0.17798
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 0.11816
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 0.00000
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 0.21533
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 1.00269
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 1.37158
i | hi | pi | P1(k) | m(k) |  |  | 
0 | 1 | 0.0625 | 0.0625 | 0.0 | 0.906510 |  | 0.84985
1 | 3 | 0.1875 | 0.2500 | 0.1875 | 2.876302 |  | 1.35425
2 | 1 | 0.0625 | 0.3125 | 0.3125 | 3.283026 |  | 0.17798
3 | 4 | 0.2500 | 0.5625 | 1.0625 | 4.159288 |  | 0.11816
4 | 0 | 0.0000 | 0.5625 | 1.0625 | 4.159288 |  | 0.00000
5 | 2 | 0.1250 | 0.6875 | 1.6875 | 3.344389 |  | 0.21533
6 | 3 | 0.1875 | 0.8750 | 2.8125 | 1.567522 |  | 1.00269
7 | 2 | 0.1250 | 1.0000 | 3.6875 | ---- |  | 1.37158
5.08984
0.81717
3.6875
em que:

## Slide 24: Otsu’s method
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
i | hi | pi | 
0 | 1 |  | 
1 | 3 |  | 
2 | 1 |  | 
3 | 4 |  | 
4 | 0 |  | 
5 | 2 |  | 
6 | 3 |  | 
7 | 2 |  | 
i | hi | pi | 
0 | 1 |  | 
1 | 3 |  | 
2 | 1 |  | 
3 | 4 |  | 
4 | 0 |  | 
5 | 2 |  | 
6 | 3 |  | 
7 | 2 |  | 
2 | 3 | 6 | 5
3 | 1 | 1 | 1
6 | 7 | 6 | 3
5 | 7 | 0 | 3
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0

## Slide 25: Otsu’s method
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
i | hi | pi | 
0 | 1 | 0.0625 | 
1 | 3 | 0.1875 | 
2 | 1 | 0.0625 | 
3 | 4 | 0.2500 | 
4 | 0 | 0.0000 | 
5 | 2 | 0.1250 | 
6 | 3 | 0.1875 | 
7 | 2 | 0.1250 | 
i | hi | pi | 
0 | 1 | 0.0625 | 
1 | 3 | 0.1875 | 
2 | 1 | 0.0625 | 
3 | 4 | 0.2500 | 
4 | 0 | 0.0000 | 
5 | 2 | 0.1250 | 
6 | 3 | 0.1875 | 
7 | 2 | 0.1250 | 
2 | 3 | 6 | 5
3 | 1 | 1 | 1
6 | 7 | 6 | 3
5 | 7 | 0 | 3
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0

## Slide 26: Otsu’s method
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
i | hi | pi | 
0 | 1 | 0.0625 | 0.906510
1 | 3 | 0.1875 | 2.876302
2 | 1 | 0.0625 | 3.283026
3 | 4 | 0.2500 | 4.159288
4 | 0 | 0.0000 | 4.159288
5 | 2 | 0.1250 | 3.344389
6 | 3 | 0.1875 | 1.567522
7 | 2 | 0.1250 | ----
i | hi | pi | 
0 | 1 | 0.0625 | 0.906510
1 | 3 | 0.1875 | 2.876302
2 | 1 | 0.0625 | 3.283026
3 | 4 | 0.2500 | 4.159288
4 | 0 | 0.0000 | 4.159288
5 | 2 | 0.1250 | 3.344389
6 | 3 | 0.1875 | 1.567522
7 | 2 | 0.1250 | ----
2 | 3 | 6 | 5
3 | 1 | 1 | 1
6 | 7 | 6 | 3
5 | 7 | 0 | 3
0.9065
2.8763
3.2830
4.1592
4.1592
3.3443
1.5675
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0

## Slide 27: Otsu’s method
7 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
i | hi | pi | 
0 | 1 | 0.0625 | 0.906510
1 | 3 | 0.1875 | 2.876302
2 | 1 | 0.0625 | 3.283026
3 | 4 | 0.2500 | 4.159288
4 | 0 | 0.0000 | 4.159288
5 | 2 | 0.1250 | 3.344389
6 | 3 | 0.1875 | 1.567522
7 | 2 | 0.1250 | ----
i | hi | pi | 
0 | 1 | 0.0625 | 0.906510
1 | 3 | 0.1875 | 2.876302
2 | 1 | 0.0625 | 3.283026
3 | 4 | 0.2500 | 4.159288
4 | 0 | 0.0000 | 4.159288
5 | 2 | 0.1250 | 3.344389
6 | 3 | 0.1875 | 1.567522
7 | 2 | 0.1250 | ----
2 | 3 | 6 | 5
3 | 1 | 1 | 1
6 | 7 | 6 | 3
5 | 7 | 0 | 3
2 | 3 | 6 | 5
3 | 1 | 1 | 1
6 | 7 | 6 | 3
5 | 7 | 0 | 3
0.9065
2.8763
3.2830
4.1592
4.1592
3.3443
1.5675

## Slide 28: Bibliography
GONZALEZ, R.C.; WOODS, R.E. Digital Image Processing. 3rd ed. Pearson, 2007.
MARQUES FILHO, O.; VIEIRA NETO, H. Processamento digital de imagens. Brasport, 1999.
  (in Brazilian Portuguese)
  Available on the author's website (for personal use only)
  http://dainf.ct.utfpr.edu.br/~hvieir/pub.html
J. E. R. Queiroz, H. M. Gomes. Introdução ao Processamento Digital de Imagens. RITA. v. 13, 2006.
  (in Brazilian Portuguese)
  http://www.dsc.ufcg.edu.br/~hmg/disciplinas/graduacao/vc-2016.2/Rita-Tutorial-PDI.pdf

## Slide 29: THE END
@misc{mari_im_proc_2023,
author = {João Fernando Mari},
title = {Image segmentation II – Thresholding},
year = {2023},
publisher = {GitHub},
journal = {Introduction to Digital Image Processing - UFV},
howpublished = {\url{https://github.com/joaofmari/SIN392_Introduction-to-digital-image-processing_2023}}
}